## Slide 1
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Supervised by
Dr. Md. Ali Hossain
Assistant Professor
Department of CSE
Rajshahi University of Engineering & Technology
Heaven’s Light is Our Guide
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Presented By
Md. Tanvir Ahmed
Roll: 123086
December 10, 2017

## Slide 2
Outline
Remote Sensing
Hyperspectral Images
Challenges of Hyperspectral Images
Motivations and Objectives
Proposed Method
Dataset Description
Feature Reduction
Experimental Analysis
Classification
Conclusion
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 3
Remote Sensing
What is remote sensing?
Acquisition of information about an object
without making physical contact with the object
Passive Remote Sensing
Active Remote Sensing
Used in geography, land surveying, military,
intelligence and planning
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Types:

## Slide 4
Remote Sensing (Contd..)
Figure: Surveillance aircraft
Figure: Remote sensing satellite
Visible and infrared range of wavelengths represents only part of the story
in remote sensing
Can also image the earth in microwave range
Figure: Electromagnetic Spectrum
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
0.4 µm – 2.5 µm

## Slide 5
Hyperspectral Images
Figure: 3D view of Hyperspectral
data cube [5]
Figure: Technical characteristics of
digital image data [2]
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 6
Challenges of Hyperspectral Images
Curse of dimensionality
Figure: Curse of dimensionality
High correlation among data
All features are not equally important
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Figure: Correlation among bands
White means 100% correlation
Black means 0% correlation

## Slide 7
Motivations and Objectives
Extract only relevant features and find an effective subspace
Address curse of dimensionality
Improve classification accuracy
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
To:

## Slide 8
Proposed Method
Feature mining:
Feature selection over feature extraction
Feature Extraction:
Principal Component Analysis (PCA)
Feature Selection:
Normalized Mutual Information (NMI)
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Target Class Oriented Subspace Detection (TCOSD)
Classifier to asses the performance:
Kernel Support Vector Machine (KSVM)

## Slide 9
Dataset Description
Dataset: AVIRIS 92AV3C
Spectral Resolution:
0.4µ m-2.5 µ m
Spatial Resolution: 30m
Band: 220
Classes:16
Data Set:
Captured Date:
June 12, 1992 Indian Pine
Test Site 3
Version 1.0
220 Band AVIRIS
Hyperspectral Image
Each band has 145 x 145 =21025 pixel
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 10
Feature Extraction
Principal Component Analysis (PCA)
Feature means unique measurable characteristics of an image/observed object
(e.g., each band)
Feature extraction means creating new features which have the essence of
original features.
Feature extraction helps to obtain relevant information from large dataset.
Perform orthogonal transformation
Data are ordered based on high variance
Dimensionality reduced by taking only first few components
Classification accuracy Increased from the original set
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 11
Feature extraction using Principal Component Analysis(PCA)
Principal Component Analysis (PCA) is a
process of reduction input dimensionality.
PC2 can be removed
Transformed data is uncorrelated
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 12
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Feature extraction using Principal Component Analysis(PCA)(Contd..)
Input the image
Subtract the mean
Calculate the covariance matrix
Calculate the eigenvectors and eigenvalues of the covariance matrix
Choose components and form a feature vector
FeatureVector = (eig1, eig2, eig3 ,…, eign)
Derive the new data set
FinalData = RowFeatureVector x RowDataAdjust
Steps of Principal Component Analysis:

## Slide 13
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Original Band
PC 1 PC 2 PC 3 PC 4
Image Band 1 Band 2 Band 3 Band 4
PCA Band

## Slide 14
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Cumulative variance of Transformed data
Figure: Cumulative variance
After principal component analysis
first 10 components have 99.75%
variance of the total

## Slide 15
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Limitations of PCA
PC 8
PC 9
PCA doesn’t consider the class structure of input data and depends solely on the global variance . Assumes high variance means high information
PC 8 has high variance but it contains
less information of image contents.
On the other hand PC 9 has low variance but it contains
more information of image contents.

## Slide 16
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Feature Selection
Mutual Information:
……..(2)
……..(1)
……..(3)
Normalized Mutual Information:
Relevant features has been selected as follows:

## Slide 17
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Normalized Mutual Information
Method | Order of selected features
Org+NMI | Band: 27,1,167,3,139,14,2,8
PCA | PC: 1,2,3,4,5,6,7,8
PCA+NMI | PC: 1,4,3,5,9,6,2,15
Table: Selected Component of Standard Approaches Studied
Figure: NMI between Class labels and Original Image bands
Figure: NMI between Class labels and Principal Components

## Slide 18
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Experimental Procedure
Proposed TCOSD method (algorithm and flow chart):
Step 1: Perform PCA and extract features of the input data set.
Step 2: Extract the training data and training label from the
PCA features.
Step 3: Consider one class as target at a time, i.e, make a class as target and all other class as background.
Step 4: Apply NMI between the training labels and the principal
components.
Step 5: Select the best principal component based on the high value of NMI. List the selected subset.
Step 6: Apply the Eq. (3) for selecting multiple features based on NMI for the target class.
Step 7: Apply the selected features to the KSVM classifier.
Step 8: Repeat step 3 to 6 by making another class as target and the remaining as background.

## Slide 19
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Selected features for all target class
Target class | Order of selected features
Hay-windrowed | PC: 4,1,17,5,12,3,16,2
Soybean-notil | PC: 1,17,16,11,20,14,13,3
Woods | PC: 1,16,17,3,15,11,5,20
Wheat | PC: 6,19,17,3,12,16,11,5
Grass/trees | PC: 4,9,5,6,16,17,2,1
Soybean-min | PC: 1,17,16,3,5,12,11,9
Corn-min | PC: 1,17,16,5,11,3,20,19
Stone-steel | PC: 3,4,1,17,16,10,5,11
Alfalfa | PC: 4,17,15,20,3,16,6,12
Grass/Pasture | PC: 9,3,17,6,16,11,1,15
Corn-notill | PC: 1,17,2,16,11,18,20,19
Soybean-clean | PC: 1,15,17,3,16,20,12,11
Corn | PC: 1,19,17,16,18,8,11,3
Bldg-Grass | PC: 15,16,17,3,18,11,19,4
Table: Selected features for all target class applying proposed method (TCOSD)
PC: Principal Component

## Slide 20
Classification
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Classification procedure:
Get train and test data
Scale data set into 0 to 1
Calculate best C and g (kernel width)for RBF
kernel of SVM. 10 fold cross validation was used
Assess the test sample accuracy. Radial basis function
(RBF) kernel was used
Class name | Train | Test
Hay-windrowed | 187 | 77
Soybean-notil | 128 | 105
Woods | 367 | 341
Wheat | 54 | 78
Grass/trees | 249 | 115
Soybean-min | 253 | 115
Corn-min | 253 | 115
Stone-steel | 36 | 30
Alfalfa | 24 | 24
Grass/Pasture | 156 | 92
Corn-notill | 172 | 60
Soybean-clean | 96 | 78
Corn | 30 | 15
Bldg-Grass | 40 | 12
Total | 1900 | 1179
Kernel support vector machine (KSVM)[3]

## Slide 21
Experimental Analysis and Conclusion
14 out of 16 classes are selected
Selected first 8 features for proposed
TCOSD gives 96.57% accuracy
Figure: Comparison of classification result of
Proposed TCOSD and standard approaches studied
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Data set | Classification Result ( First 8 features only)
Org+NMI | 72.26%
PCA | 89.90%
PCA+NMI | 93.12%
TCOSD (Proposed) | 96.57%
Data set | C | g
Org+NMI | 10 | 2.44
PCA | 19 | 2.40
PCA+NMI | 16 | 0.7
TCOSD (Proposed) | 5 | 0.75

## Slide 22
Conclusion
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
A better subspace is detected than other standard approaches
Can provide best classification accuracy
Proposed method is most suitable for ground object detection and identification

## Slide 23
Future Work
Proposed method needs some further improvement
    To handle complex class relationships
Subspace detection can be performed by introducing adaptive thresholding T.
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification

## Slide 24
Acknowledgement
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Special thanks to
Professor Dr. David A. Landgrebe, Purdue University
For the dataset and MultiSpec

## Slide 25
References
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
[1]L. I. Smith, “A tutorial on Principal Component Analysis”, February 26,2002.
[2]J. A. Richards and X. Jia, Remote Sensing Digital Image Analysis 4th edition,
Verlag: Springer 2006.
[3]C. Hsu, C. Chang, and C. Lin,Department of Computer Science,National Taiwan University,
Taipei 106, Taiwan,"A Practical Guide to Support Vector Classication",
Initial version: 2003, Last updated: May 19, 2016.
[4]M. A. Hossain, X. Jia and M. Pickering, “Subspace detection using a mutual-information measure
for hyperspectral image classification,” IEEE Geoscience and Remote Sensing Letters,
vol. 11, no. 2, pp. 424-428, Feb. 2014.
[5][Online]https://en.wikipedia.org/wiki/Hyperspectral_imaging

## Slide 26
References
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
26/27
[6] M. A. Hossain, X. Jia and M. Pickering, “ Improved feature selection based on a mutual information measure for hyperspectral image classification," IEEE International Geoscience and Remote Sensing Symposium (IGARSS), Munich, Germany, pp. 3058-3061, Jul. 2012.
[7] M. A. Hossain, M. Pickering and X. Jia, “ Unsupervised feature extraction based on a mutual
information measure for hyperspectral image classification," IEEE International Geoscience and
Remote Sensing Symposium (IGARSS),Vancouver, Canada, pp. 1720-1723, Jul. 2011.
[8] C. Chang and C. Lin, “LIBSVM: A library for support vector machines,” ACM Trans. Intell. Syst. Technol., vol. 2, no. 3, pp. 27:1–27:27, Apr. 2011.

## Slide 27
Target Class Oriented Subspace Detection for Effective Hyperspectral Image Classification
Thank You